IP/ROP Project

For the purpose of the architecture in the project, the 16-bit wordsize was chosen as it is a convenient size to work with. It is sufficient size for an instruction, and not so large as to become problematic in terms of FPGA size, as 32 bit multipliers and other circuits may be.

Instruction Format
OPCODE	A	B	Immediate
5 bits	3	3	5

Register Specifications

Register	Description	ID
zero	Zero Register, mapped to zero	0
A	Accumulator Register, output of arithmetic goes here.	1
B-D	General Purpose Registers	2,3,4
SP	Stack Pointer, this holds the base of the stack, if zero stack operations interrupt.	5
DS	Segmentation Register, used to offset memory access
K	Kernel Register, stores 1/4th the value above which memory is reserved for user space.	7
IP	Instruction Pointer, Internal	N/A

One important note about the registers, is there exists a 0 register, which is hardcoded to the value 0, which is useful for a number of instructions that use an immediate, to allow for adding 0 plus the immediate for instance, rather than having to zero a register in use for that.

Another important thing to notice, is the register IP does not exist in the register file, and instead exists separately, preventing many instructions from modifying it directly. Branch instructions or instructions such as call or return are needed to modify it.

Instruction Set

Instruction	Assembly	Description	opcode
swap	SWAP A,B	Swaps the value of two registers
halt	HLT	Halts the execution until interrupted
jmp	JMP [ADDR]	Changes the IP to be equal to the IP minus
push	PUSH A	Decrements SP, and adds the value of A into the stack.
pop	POP A	Puts the current value on the stack into A, then increments stack
add	ADD A, B <Immediate>	Accumulator = A + B + Imm
subtract	SUB A, B <Immediate>	Accumulator = A - (B*Imm)
multiply	MUL A, B <Immediate>	Accumulator = A * (B+Imm)
or	OR A,B <Immediate>	Accumulator = A | B | Imm
xor	XOR A,B <Immediate>	Accumulator = A ^ (B | Imm)
and	AND A, B <Immediate>	Accumulator = A & (B | Imm)
modulo	MOD A, B	Accumulator = A % B
random	RAND A, B	Accumulator is set to a random value from 1 to value in B
Read IO	readw A, B	Reads IO device at io addr stored in A into B
Write IO	writew A, B <imm>	Writes from B to IO device stored at A plus imm
call	call [addr]	Adds the address of the next instruction to the stack, and then jumps to the addr
ret	ret	Returns to the address stored in stack
branch greater or equal to	bge A,B [offset]	If A >= B, it moves the IP forward offset*4 bytes. Else, nothing.

Memory Map: