IP/ROP Project

For the purpose of the architecture in the project, the 16-bit wordsize was chosen as it is a convenient size to work with. It is sufficient size for an instruction, and not so large as to become problematic in terms of FPGA size, as 32 bit multipliers and other circuits may be.

The Instruction format is fairly simple, and flexible. With a fixed instruction size of 16-bits, it is often better to have multiple instruction types, but for convenience one was chosen. The use of a segmentation register removes the memory limitations of the 5 bit immediate, but there are still other problems that arise. For instance, loading an arbitrary word would take three immediate values.

Instruction Format
OPCODE	A	B	Immediate
5 bits	3	3	5

Register Specifications

Register	Description	ID
zero	Zero Register, mapped to zero	0
A	Accumulator Register, output of arithmetic goes here.	1
B-D	General Purpose Registers	2,3,4
SP	Stack Pointer, this holds the base of the stack, if zero stack operations interrupt.	5
DS	Segmentation Register, used to offset memory access. Appended to 5-bit immediate, so should not be greater than 11 bits.	6
K	Kernel Register, stores 1/2th the value above which memory is reserved for user space.	7
IP	Instruction Pointer	N/A
EIP	Exception Instruction Pointer	N/A
IVR	Stores address of interrupt vector table, each entry being one word long. (Will usually be a jump.)	N/A
IVL	Stores the length of interrupt vector table, in entries.	N/A

One important note about the registers, is there exists a 0 register, which is hardcoded to the value 0, which is useful for a number of instructions that use an immediate, to allow for adding 0 plus the immediate for instance, rather than having to zero a register in use for that.

All addresses that are used in the immediate will be combined with the DS to produce the address.

Another important thing to notice, is the register IP does not exist in the register file, and instead exists separately, preventing many instructions from modifying it directly. Branch instructions or instructions such as call or return are needed to modify it.

Security note. For the purpose of security, there are two regions or segments of memory. The kernel segment and user segment. The user segment may not call, jump read or modify the kernel memory in anyway, nor modify the kernel register. The kernel register's value times two defines the region above which is userspace.

Instruction Set

Instruction	Assembly	Description	opcode
swap	SWAP A,B	Swaps the value of two registers
halt	HLT	Halts the execution until interrupted
jmp	JMP [ADDR]	Changes the IP to be equal to the IP minus
push	PUSH A	Decrements SP, and adds the value of A into the stack.
pop	POP A	Puts the current value on the stack into A, then increments stack
add	ADD A, B <Immediate>	Accumulator = A + B + Imm
subtract	SUB A, B <Immediate>	Accumulator = A - (B+Imm)
multiply	MUL A, B <Immediate>	Accumulator = A * (B+Imm)
left bitshift	SHL A,B + Imm	Accumulator = A << (B+Imm)
Right bitshift	SHR A,B + Imm	Accumulator = A >> (B+Imm)
or	OR A,B <Immediate>	Accumulator = A | B | Imm
xor	XOR A,B <Immediate>	Accumulator = A ^ (B | Imm)
and	AND A, B <Immediate>	Accumulator = A & (B | Imm)
modulo	MOD A, B	Accumulator = A % B
random	RAND A, B	Accumulator is set to a random value from 1 to value in B
Read IO	readw A, B	Reads IO device at io addr stored in A into B
Write IO	writew A, B <imm>	Writes from B to IO device stored at A plus imm
call	call A	Adds the address of the next instruction to the stack, and then jumps to the address in A
ret	ret	Returns to the address stored in stack
branch greater or equal to	bge A,B [offset]	If A >= B, it moves the IP forward offset instructions. Else, nothing.
interrupt	int A imm	Creates interrupt at A+imm.
Interrupt return	iret	Leaves interrupt, and returns to the code that was being executed.
Load Word	loadw [A + Imm]	Loads one word pointed to by A+imm into accumulator
Store Word	stow [A + Imm]
Load Interrupt Vector Table	livt A, Imm	Loads table of interrupts at position addressed by A, and loads exactly Imm interrupts.

Flag	Meaning
IOorMem	If high, the multiplexer will direct memory accesses to the IO bus instead
Except	If high, EIP will preserve the IP. IP will also be set to IVR + (interrupt #), with a maximum value of IVL + IVR. Otherwise, the general exception interrupt # will be called

Exception and Interrupt handling procedure:

If any exception flag is high, then IP will be saved into the EIP. IP will then be changed to be equal to IVR + interrupt #, where the interrupt number is determined by the flag raised, or by what the value of the accumulator was after an INT instruction. If IVR + interrupt # is greater than IVL, it will result in interrupt 0 being called instead.

Interrupt #	Sources and Meaning
0	General Interrupt, called whenever the interrupt address is invalid
1	Invalid Access, this interrupt is called whenever a point above the K register, tries to read or modify kernel space.
2	Arithmetic Error, this interrupt is called whenever there is a divide by zero, or similar issue.